## Slide 1: Detection of meteors in broad daylight: a feasibility study
Jérémie Vaubaillon (IMCCE)
Sylvain Rommeluere, Pierre Simoneau (ONERA)

## Slide 2: Introduction / questions
Rossano et al., 2001 (from a few frames) concluded meteors emit 25 times more energy in M-IR band [3;5] μm than in visible band
  => Q1: how do meteors emit light in M-IR band?
Sky brightness decreases with altitude
  => Q2: How dark is the sky in M-IR band as a function of altitude?
Q3: Can we detect meteors in broad daylight? IOW: what is the S/N for meteors in M-IR?

## Slide 3: Q1: how do meteors emit light in M-IR band?
Bilanga
M-IR
Visible
Stannern
Rommeluere et al. 2024: Black body at ~2000 K emission
Very ≠ from Rossano et al., 2001…
Notes: Black body emission
Sample behaviour similar in M-IR and Visible
Light curve in M-IR somewhat similar to Visible, but sometimes show slower rise
Max sample Temperature [1800 - 2500] K ; from Vis to N-IR spectra and from M-IR (alone) measurements

## Slide 4: Q2: How dark is the sky in M-IR band?
Sky brightness
At night, from ground
Sky brightness
At noon, from 20 km of altitude
Calculations performed with Rayjn software (Simoneau et al., 2017)

## Slide 5: Computation of S/N at the pixel Voltage level (1/2)
Input
  M-IR instrument: F=100 mm f/2, QE=0.8, exptime=5 ms (20 fps), Tsensor = 80 K ; readout + dark noises
  Target : 1 cm3 ; Black body emission at 2000 K (conclusion from wind tunnel experiment) ; distance=f(geometry) ; Alt=100 km ; NOT resolved by camera+lens
  Sky brightness and transmission computations: Alt=[15,20,30,40] km ; Az=[0,90,180] deg, El=[10,30,45,70,80] deg ; dates=winter, summer

## Slide 6: Computation of S/N at the pixel Voltage level (2/2)
Compute:
  Sky transmission and luminance (=background) as well as meteoroid luminance [ph.m-2.s-1] => Convert to photo-electrons
  Instrument signal (readout, dark, sky, meteor) at pixel level
  Tension V at pixel created by each contributor (noise, sky, meteor)
  S/N = Vmeteor / (Vsky + Vnoise)

## Slide 7: Luminances and transmission
Sky
Meteor
Winter ; Alt=20 km, Az=90 deg, El=45 deg

## Slide 8: S/N over the whole M-IR band
El=10 deg
El=30 deg
El=45 deg
El=80 deg
Az=0 deg
Az=90 deg
Az=180 deg

## Slide 9: The culprit…
Winter
Summer

## Slide 10: Q4: can we narrow down the spectral band? Spectrally resolved S/N
Winter
Alt=20 km, Az=90 deg, El=45 deg
Winter
Alt=40 km, Az=180 deg, El=70 deg

## Slide 11: Conclusion
M-IR detection of meteors is feasible under restricted conditions
The driving factor is the physical distance between the meteoroid and the camera, because of Black body radiation of meteoroid in M-IR band
Assumption of point-like source might not hold in case of meteoroid disruption