## Slide 1
High-Speed Lenses in Astronomy
Prof. Dr.-Ing. Peter C. Slansky
Department II Technology
University for Television and Film Munich
IMC 2024 Kutná Hora

## Slide 2
My first Video Meteor Observation: Camelopardalids 2014
Canon C300 with Zeiss Distagon 1.2/18mm (35mm film)
IMC 2024 Kutná Hora
DEP = 15 mm

## Slide 3
Why High-Speed Lenses?
IMC 2024 Kutná Hora

## Slide 4
Why High-Speed Lenses?
IMC 2024 Kutná Hora
For a shallow depth of field with a “pleasing” bokeh

## Slide 5
Early High-Speed Lenses for Photography
IMC 2024 Kutná Hora
www.leica-camera.com/de
1961

## Slide 6
IMC 2024 Kutná Hora
Canon 7 with
0.95/50mm
7 elements in 5 groups
1961
www.bluemooncameracodex.com
Early High-Speed Lenses for Photography

## Slide 7
IMC 2024 Kutná Hora
Zeiss
Super-Q-Gigantar
0.33/40mm
1966
“Q” for “Quatsch”…
Early High-Speed Lenses for Photography
www.zeiss.de

## Slide 8
Early High-Speed Lenses in Cinema
IMC 2024 Kutná Hora
Zeiss Planar 0.7/50mm
1967
www.zeiss.de
www.rikuwrites.blogspot.com
Barry Lyndon (Director: Stanley Kubrick)
1975

## Slide 9
In Astronomy we do not have a depth of field
IMC 2024 Kutná Hora
So, we do not see the bokeh
High-Speed Lenses in Astronomy

## Slide 10
Relevant Optical Parameters
Focal lenght Distance between primary plane of lens and focal point [mm]  Image (de-)magnification
Image circle Diameter of sharp image [mm]  Camera sensor diagonal has to fit into this
Field of view Angular dimensions of the image, given by focal length and sensor size [° x °]  Angular image dimensions
Aperture (Entry Pupil) Size of the free opening of the lens, expressed by its diameter DEP or area AEP  Light distribution of the lens / Brightness of pointshaped objects
F-stop Quotient between focal lenght and diameter of the aperture F = f / DEP  Brightness of areal objects
Speed Smallest F-number/largest aperture of the lens  What it is all about here…
IMC 2024 Kutná Hora

## Slide 12
The „Meteors high-speed dilemma“:
For faint meteors we want a large aperture.
This usually comes with a higher focal length.
That means a smaller field of view.
So, we get less meteors…

## Slide 13
The High-Speed Dilemma: Aperture vs. Field
- 1.4/24mm
73° x 45.4°
DEP = 17.1 mm
1.4/85mm
23.6° x 13.5°
DEP = 60.7 mm
/
2.8/400mm
5.1° x 2.9°
DEP = 143 mm
\
267 meteors
in 2 hrs
93 meteors
in 2 hrs
21 meteors
in 2 hrs
IMC 2024 Kutná Hora
Quadrantids 2020

## Slide 14
High-Speed Lenses for small Sensor Cameras
IMC 2024 Kutná Hora
De Oude, Delft
Rayxar
0.75/50mm
0.75/65mm
Photo: Sirko Molau
DEP 50 = 67 mm
DEP 65 = 87 mm

## Slide 15
High-Speed Cine Lenses for full Format Cameras
IMC 2024 Kutná Hora
Zeiss Planar
1.4/50mm
1.4/85mm
DEP 50 = 35 mm
DEP 85 = 60,7 mm

## Slide 16
Accumulation of Apertures: Plywood Camera Battery
Up to 13 analog SLRs
Canon T-70 with
Canon FD 1.8/50mm lenses and central timer
40° x 27° field
DEP = 27,8 mm x 13 75 % efficiency:
IMC 2024 Kutná Hora
DEP eff = 87 mm

## Slide 17
Accumulation of Apertures: All Sky 7
7 cameras with 1.0/4mm lenses; 45° x 80° field
DEP = 4 mm x 7
81,2 % efficiency:
IMC 2024 Kutná Hora
DEP eff = 9.5 mm
www.allsky7.net

## Slide 18
Accumulation of Apertures: All Sky Twin 4K²
2 Sony a7S with
2 Samyang 2.8/14mm
fisheye lenses
on shift adapters
DEP = 5 mm x 2
82 % efficiency:
IMC 2024 Kutná Hora
DEP eff = 6.4 mm
- Low speed
- Uniform brightness
- Uniform distortion

## Slide 19
Precision HD-8 1.0/140 mm
Projection lens
CRT video beamer
High-Speed Lenses of the Author
Zeiss 0.77/50mm
Projection lens
16mm
Sony GM 1.2/50mm
Photo lens
Full format
Sony GM 1.4/24mm
Photo lens
Full format
Angenieux
1.3/25mm
film lens
16mm
Zeiss 1.2/35mm
Film lens
35mm
Canon FD
1.4/50mm
Photo lens
Full format
IMC 2024 Kutná Hora

## Slide 20
High-Speed Lenses
IMC 2024 Kutná Hora
Is there a physical speed limit?
www.dg77.net/photo/tech/fastex.htm

## Slide 21
High-Speed Lenses: What’s the Problem?
IMC 2024 Kutná Hora
Aperture
Field
Uniformity of
brightness
Uniformity of
resolution
Freedom of
distortion
Image
planarity
Resolution
Contrast

## Slide 22
High-Speed Lenses: Dream on…
IMC 2024 Kutná Hora
Aperture
Field
Uniformity of
brightness
Uniformity of
resolution
Freedom of
distortion
Image
planarity
Resolution
Contrast

## Slide 23
High-Speed Lenses: Reality I
IMC 2024 Kutná Hora
Aperture
Field
Uniformity of
brightness
Uniformity of
resolution
Freedom of
distortion
Image
planarity
Resolution
Contrast

## Slide 24
High-Speed Lenses: Reality I
IMC 2024 Kutná Hora
Aperture
Field
Uniformity of
brightness
Uniformity of
resolution
Freedom of
distortion
Image
planarity
Resolution
Contrast

## Slide 25
High-Speed Lenses: a practical Quality Test
IMC 2024 Kutná Hora
Sirius in image centre
\
Sirius in image corner
/

## Slide 26
High-Speed Lenses: a practical Quality Test
Sony GM 1.2/50mm
2020
Zeiss Planar 1.4/50mm
1980
Canon FD
1.4/50mm
1970
Centre
Corner
Sirius
IMC 2024 Kutná Hora

## Slide 27
High-Speed Lenses for Meteor Observation
Conclusions:
Aperture counts – but also field of view
There is no magic stick: if the lens design is subordinated to speed or aperture alone, the other criteria will inevitably suffer (given the budget)
A cheap lens with ultra-high-speed will always have strong artefacts, brightness fall-off and distortion
High image quality from the centre to the corner at F stops 1.2 to 1.4 for full-frame or APS-C comes at a price
Lenses with good correction of all image quality parameters are preferable – even for the price of a F-stop
For astronomic ultra-wide-field imaging such as Meteor observation multi-aperture systems are interesting
IMC 2024 Kutná Hora
Photo with Sony GM 1.2/50mm at F = 1.2 with Sony α7S at ISO 6.400 and t = 4 s

## Slide 28
Thank You very much for Your attention !
High-Speed Lenses in Astronomy
Prof. Dr.-Ing. Peter C. Slansky
Department II Technology
University for Television and Film Munich
IMC 2024 Kutná Hora
References:
Slansky, Peter C.: High speed lenses in Astronomy; WGN journal of the IMO 52:1 (2024)
Slansky, Peter C.: Einführung in die fotografische Optik II: Blende und Tiefenschärfe; script at HFF Munich
www.peter-slansky.de
https://leica-camera.com/de-DE/fotografie/objektive/m/noctilux-m-1-12-50mm-asph-schwarz#
https://bluemooncameracodex.com/technical-reviews/living-with-the-canon-50mm-f095-dream-lens
https://rikuwrites.blogspot.com/2010/06/most-beautiful-movie-ever-made.html
www.dg77.net/photo/tech/fastex.htm
https://blog.ormsdirect.co.za/the-worlds-fastest-fake-lens-zeiss-40mm-f0-33/
https://allsky7.net